## Slide 1: FPGA-based Real-Time Learning Architecture with Partial Reconfiguration for Spiking Neural Networks
Yike Jing
Dresden, Germany. October 7, 2026
Supervisors: Gloria Sepanta, Dr.-ing. Lester Kalms
Institute of Computer Engineering – Chair of Adaptive Dynamic Systems
Master Thesis

## Slide 2: Contents
1 Introduction & Motivation
2 Related Work
3 Background
4 Design & Implementation
5 Results
6 Conclusion & Outlook
Slide 2/29

## Slide 3: Introduction & Motivation
01
Slide 3/29

## Slide 4: Motivation and Research Problem
Slide 4/29
Motivation
Why SNNs? Spike timing carries temporal information. Sparse activity offers potential for efficient edge processing.
Why online learning? Adapt weights on the device as new data arrives, reducing the need for offline retraining.
Problem
Baseline Spiker+ deploys weights prepared offline, which remain fixed during inference.
Integrating SDSP requires writable weights and correct state and write-back timing within the inference schedule.

## Slide 5: Related Work
02
Slide 5/29

## Slide 6: Related Work
Work | [1] ODIN Frenkel et al. (2019, TBioCAS) | [2] MorphIC Frenkel et al. (2019, TBioCAS) | [3] Asgari et al. (2020, IJCTA) | [4] Li et al. (2021, TCAS-I) | [5] TEDOP Shi et al. (2022, ICTA) | [6] RAINE Fang et al. (2022, A-SSCC) | This Work
Platform and scale | 28 nm ASIC 256 neurons 64k synapses | 65 nm ASIC 2,048 neurons >2M synapses | Spartan-6 LX45 2 neurons 1 plastic synapse | VC707, Virtex-7 984 neurons 88.4k synapses | Zynq-7010 Up to 1,024 × 10 | Alveo U250 16 UDLEs | PYNQ-Z1, XC7Z020 10 neurons 7,840 plastic synapses
Neuron model | 8-bit LIF / Izhikevich-like | LIF | LIF + CAVE Ca estimator | LIF | 16-bit TI (non-spiking) | LIF | Modified LIF subtractive reset
SNN model (topology) | 256–10 fully connected | 4 conv. kernels + pooling + FC–8 | 2-neuron minimum network | 784 input 100 excitatory + 100 inhibitory | 784–10 fully connected | 251–100–4 SFNN 256–100–2 SRNN 784–1000–10 SCNN | 784–10 fully connected
On-chip learning (algorithm) | SDSP (teacher-supervised) | Stochastic S-SDSP | High-precision SDSP | Trace-based STDP (unsupervised) | S4DSP (supervised) | Rewarded Trace-STDP | SDSP (teacher-supervised)
Dataset | MNIST (16 × 16) | 8-pattern benchmark | Synthetic spikes (no dataset) | MNIST | MNIST | MIT-BIH ECG CHB-MIT EEG MNIST | MNIST
Slide 6/29

## Slide 7: Background
03
Slide 7/29

## Slide 8: Spiker+ Framework
Slide 8/29
[7] A. Carpegna et al, "Spiker+: A Framework for the Generation of Efficient Spiking Neural Networks FPGA Accelerators for Inference at the Edge," in IEEE Transactions on Emerging Topics in Computing. 2025,

## Slide 9: Architecture of SNN Accelerator from Spiker+
[7] A. Carpegna et al, "Spiker+: A Framework for the Generation of Efficient Spiking Neural Networks FPGA Accelerators for Inference at the Edge," in IEEE Transactions on Emerging Topics in Computing. 2025,
Slide 9/29

## Slide 10: Spike-Driven Synaptic Plasticity
Neuron Model:
Calcium Variable:
Learning Conditions:
1. Presence of a presynaptic spike: Jump
2. Absence of a spike: Bistability
SYMBOL LEGEND
V(t)
Neuron membrane potential
C
Calcium variable
w
Synaptic weight
θₘ
Membrane-voltage threshold
θ₁, θ₂, θ₃
Calcium-variable thresholds
λ
Membrane leakage term
I(t)
Input current at time t
t_pre
Presynaptic spike arrival time
spk_post
Postsynaptic-spike indicator
time_ref
Reference event for C decay
bist
Bistability control signal
n; w[n−1]
Weight width; most-significant bit
Slide 10/29

## Slide 11: Design & Implementation
04
Slide 11/29

## Slide 12: Online-Learning Integration
Slide 12/29
Weight memory
Neurons
SDSP update
Input spikes
Output spikes
Neuron state
Write-back
Events
Read weight
SDSP updates stored weights for inference.

## Slide 13: Digital Weight-Update Datapath
Slide 13/29

## Slide 14: Address-Aligned Weight Write-Back
Slide 14/29
Keep each updated weight paired with its original address.
Weight write-back overlaps with the next weight read.
Read
weight k
Update
weight k
Write back
to address k

## Slide 15: PYNQ-Z1 System Integration
Control
AXI4-Lite registers
Input transfer
DDR, DMA and stream FIFO
Hardware
SNN–SDSP accelerator IP
Slide 15/29

## Slide 16: Verification Overview
Slide 16/29
RTL checks: learning logic and weight-memory behavior.
Board checks: interfaces, outputs and software–hardware behavior.
Learning checks: persistent updates and three complete training epochs.
PYNQ Z1
[8] Digilent Inc. PYNQ-Z1: Python Productivity for Zynq-7000 ARM/FPGA SoC. URL: https://digilent.com/shop/pynq-z1-python-productivity-for-zynq-7000-arm-fpga-soc/

## Slide 17: Dynamic Partial Reconfiguration (DPR)
Slide 17/29
Only SDSP was implemented. No runtime switching between learning rules was required.
SDSP is coupled to neuron state, synaptic memory and layer timing.
DPR would require a common interface, state preservation and additional verification.
Final implementation: static configuration with runtime learning control.

## Slide 18: Results
05
Slide 18/29

## Slide 19: Resource Utilization, Overhead and Power
Post-implementation results on XC7Z020
Resource | Pure Spiker | SNN + SDSP system | Difference | Change
LUT | 1,780 (3.35%) | 5,056 (9.50%) | +3,276 | +184.0%
FF | 1,829 (1.72%) | 5,294 (4.98%) | +3,465 | +189.4%
BRAM | 1.50 (1.07%) | 4.00 (2.86%) | +2.50 | +166.7%
BUFG | 1 (3.13%) | 1 (3.13%) | 0 | 0.0%
Slide 19/29
Resource differences include learning and system integration.
Vivado post-implementation power estimate
Total on-chip | Dynamic | Static | PS7 dynamic
1.445 W | 1.309 W | 0.136 W | 1.260 W
Complete Zynq device, medium-confidence estimate. PS7 dominates dynamic power.

## Slide 20: Evaluation Configuration
Parameter | Fixed value
Network / neuron | 784–10, modified subtractive-reset LIF
Membrane / excitatory weight | 16-bit signed Q9 state / 3-bit unsigned weight
Spike encoder | Spiker+ rate coding, gain 0.1
Window / stream size | 100 steps, 2,500 words, 10,000 bytes per image
Teacher current | 128 in Q9 = 0.25
Calcium leakage / bistability | Once every 10 steps / disabled
Training seeds / validation seed | 2028, 2029, 2030 / 2027
Slide 20/29

## Slide 21: MNIST Evaluation Protocol
Slide 21/29
Training: 60,000 images per epoch. Learning and teacher input enabled.
Initial
evaluation
Train
Epoch 1
Evaluate
Train
Epoch 2
Evaluate
Train
Epoch 3
Evaluate
Evaluation: reuse 1,000 class-balanced images with fixed spike encoding. Learning and teacher input disabled.
One bitstream load. Learned weights persist across all three epochs.

## Slide 22: Accuracy and Output Activity
Slide 22/29
Chart: Strict vs Active-image Validation Accuracy
| 0 (initial) | 1 | 2 | 3
Strict accuracy (all images) | 0.059 | 0.32 | 0.363 | 0.396
Active-image accuracy (non-silent) | 0.0761 | 0.5161 | 0.5056 | 0.5045
Silent / 1,000: Initial 225, Epoch 1: 380, Epoch 2: 282, Epoch 3: 215.
Later gains in strict accuracy mainly reflect fewer silent images.

## Slide 23: End-to-End Runtime
Chart: Images/s
| Training | Inference
Images per second | 66.16 | 67.77
training transactions
in 45 min 20.77 s
Slide 23/29
Includes Python control, DMA, register access and a 10 ms delay/image

## Slide 24: Quantitative Comparison
Slide 24/29
Work | [1] ODIN Frenkel et al. (2019, TBioCAS) | [2] MorphIC Frenkel et al. (2019, TBioCAS) | [3] Asgari et al. (2020, IJCTA) | [4] Li et al. (2021, TCAS-I) | [5] TEDOP Shi et al. (2022, ICTA) | [6] RAINE Fang et al. (2022, A-SSCC) | This Work
Platform and scale | 28 nm ASIC 256 neurons 64k synapses | 65 nm ASIC 2,048 neurons >2M synapses | Spartan-6 LX45 2 neurons 1 plastic synapse | VC707, Virtex-7 984 neurons 88.4k synapses | Zynq-7010 Up to 1,024 × 10 | Alveo U250 16 UDLEs | PYNQ-Z1, XC7Z020 10 neurons 7,840 plastic synapses
Neuron model | 8-bit LIF / Izhikevich-like | LIF | LIF + CAVE Ca estimator | LIF | 16-bit TI (non-spiking) | LIF | Modified LIF subtractive reset
SNN model (topology) | 256–10 fully connected | 4 conv. kernels + pooling + FC–8 | 2-neuron minimum network | 784 input 100 excitatory + 100 inhibitory | 784–10 fully connected | 251–100–4 SFNN 256–100–2 SRNN 784–1000–10 SCNN | 784–10 fully connected
On-chip learning (algorithm) | SDSP (teacher-supervised) | Stochastic S-SDSP | High-precision SDSP | Trace-based STDP (unsupervised) | S4DSP (supervised) | Rewarded Trace-STDP | SDSP (teacher-supervised)
Dataset | MNIST (16 × 16) | 8-pattern benchmark | Synthetic spikes (no dataset) | MNIST | MNIST | MIT-BIH ECG CHB-MIT EEG MNIST | MNIST
Resources / area | 0.086 mm² | 2.86 mm² | 450 LUTs 249 registers | N/R | 952 LUTs 741 FF 4 BRAM | 21,560 LUTs* 20,863 FF* | 5,056 LUTs 5,294 FF 4 BRAM
Frequency | 75 MHz | 55 MHz | 131 MHz | 100 MHz | 250 MHz | 75 MHz | 100 MHz
Accuracy | 85.0% rate 84.5% rank-order | 100% patterns (800/800) | N/A No classifier | 85.28% online 82.52% relearning | 90.4% MNIST test | 98.26% MNIST | 39.6% fixed validation 3 epochs

## Slide 25: Conclusion & Outlook
06
Slide 25/29

## Slide 26: Conclusions
Slide 26/29
Hardware contribution
Synthesizable SDSP, ten learning lanes and address-aligned writable synapses.
System contribution
Reusable Spiker+ extension on PYNQ-Z1 at 100 MHz, with 180,000 continuous training transactions.
Strict validation accuracy: 5.9% to 39.6% after three epochs
Epoch 1 improves classification among active images. Later gains mainly reflect fewer
silent images (380 to 215), with active-image accuracy remaining near 50%.
Accuracy remains an intermediate result
Convergence is unestablished and class responses remain unstable. Single-layer capacity
and 3-bit weights may constrain accuracy, but their individual effects are untested.

## Slide 27: Limitations and Next Experiments
Slide 27/29
Training scope: one run over three epochs. Extend training and repeat runs across parameter settings.
Validation: the fixed validation set guided continuation. Use an untouched final test set.
Model capacity: one layer with 3-bit weights. Explore higher precision and larger networks.
Performance and energy: application runtime and estimated power. Add cycle counters and measure board energy per image.

## Slide 28: References
[1] C. Frenkel, M. Lefebvre, J. -D. Legat and D. Bol, "A 0.086-mm 2 12.7-pJ/SOP 64k-Synapse 256-Neuron Online-Learning Digital Spiking Neuromorphic Processor in 28-nm CMOS," in IEEE Transactions on Biomedical Circuits and Systems, vol. 13, no. 1, pp. 145-158, Feb. 2019, doi: 10.1109/TBCAS.2018.2880425.
[2] Frenkel, Charlotte, Jean-Didier Legat, and David Bol. "MorphIC: A 65-nm 738k-synapse/mm $^ 2$ quad-core binary-weight digital neuromorphic processor with stochastic spike-driven online learning." IEEE transactions on biomedical circuits and systems 13.5 (2019): 999-1010.
[3] Asgari H, Mazloom-Nezhad Maybodi B, Sandamirskaya Y. Digital multiplier-less implementation of high-precision SDSP and synaptic strength-based STDP. Int J Circ Theor Appl. 2020; 48: 724–738.
[4] S. Li, Z. Zhang, R. Mao, J. Xiao, L. Chang and J. Zhou, "A Fast and Energy-Efficient SNN Processor With Adaptive Clock/Event-Driven Computation Scheme and Online Learning," in IEEE Transactions on Circuits and Systems I: Regular Papers, vol. 68, no. 4, pp. 1543-1552, April 2021, doi: 10.1109/TCSI.2021.3052885.
[5] C. Shi et al., "TEDOP: A Tiny Event-Driven Neural Network Hardware Core Enabling On-Chip Spike-Driven Synaptic Plasticity," 2022 IEEE International Conference on Integrated Circuits, Technologies and Applications (ICTA), Xi'an, China, 2022, pp. 62-63, doi: 10.1109/ICTA56932.2022.9963064.
[6] C. Fang, F. Tian, C. Wang, J. Yang and M. Sawan, "A 217.8 MSOPs/W FPGA-based Online Learning SNN Processor Using Unified Event-Driven Structure and Topology Aware Data Reuse Strategies," 2022 IEEE Asian Solid-State Circuits Conference (A-SSCC), Taipei, Taiwan, 2022, pp. 1-3, doi: 10.1109/A-SSCC56115.2022.9980727.
[7] A. Carpegna, A. Savino and S. D. Carlo, "Spiker+: A Framework for the Generation of Efficient Spiking Neural Networks FPGA Accelerators for Inference at the Edge," in IEEE Transactions on Emerging Topics in Computing, vol. 13, no. 3, pp. 784-798, July-Sept. 2025, doi: 10.1109/TETC.2024.3511676.
[8] Digilent Inc. PYNQ-Z1: Python Productivity for Zynq-7000 ARM/FPGA SoC. URL: https://digilent.com/shop/pynq-z1-python-productivity-for-zynq-7000-armfpga-soc/
Slide 28/29

## Slide 29: Thank you!
Slide 29/29

## Slide 30: Backup: Write-Back Timing
The update for W[k] must return to address k while the read pipeline advances.
Registered address and pending-write state preserve the final excitatory update
Backup 1/6

## Slide 31: Backup: Verification Details
Level | Question | Evidence
RTL modules | Are local operations correct? | Thresholds, bounded updates and RAM behaviour
Integrated interfaces | Is a transaction complete? | 2,500 words and 100 accepted/completed steps
Board controls | Does the deployed path match? | Register read-back, zero and dense inputs
Persistent learning | Does training affect later inference? | Teacher control and bitstream reload
Full workload | Does operation remain continuous? | Three epochs, 180,000 training transactions
Backup 2/6

## Slide 32: Backup: Functional Evidence
Check | Observed evidence
Zero-input board transaction | 100 accepted steps, all output counts zero
Dense-input board transaction | 100 accepted steps, 99 spikes per output neuron
Teacher-controlled persistent test | 5/10 output vectors changed only at target neuron 7
Aligned software / hardware baseline | 4 silent samples each, 5/10 exact count vectors
Long-run operation | 180,000 supervised transactions over three epochs
Backup 3/6

## Slide 33: Backup: Persistent Learning on the FPGA
Later inference changes with the teacher off, and bitstream reload restores baseline
Backup 4/6

## Slide 34: Backup: Per-Class Learning Behavior
Backup 5/6

## Slide 35: Backup: snn_axi_wrapper
Backup 6/6
snn_axi_wrapper
AXI4-Stream
from DMA/FIFO
PS: AXI4-Lite
IRQ to PS
AXI4-Lite registers
Configuration
Status and results
Transaction & event control
Start and reset
Learning events
Stream unpacker
25 × 32-bit
words per step
Ping-pong buffers
2 × 784-bit
network_sdsp
784-input SNN
with SDSP
Output processing
10 spike counters
Sequential argmax
Control / ready
Results
Two buffers overlap input loading with network processing.
AXI4-Lite provides runtime control and reads back counts and class.
Functions inside the wrapper. network_sdsp is the instantiated core.